The full heat conduction equation in 1D with transient conditions and a heat source (q) included is a partial differential equation (PDE) and is given by:
∂t∂T​=α∂x2∂2T​+kq(x)​
Where:
- ∂t∂T​ is the rate of change of temperature with respect to time (in degrees Celsius per second, s°C​).
- α is the thermal diffusivity of the material (in square meters per second, sm2​).
- ∂x2∂2T​ is the second spatial derivative of temperature with respect to position (in degrees Celsius per square meter, m2°C​).
- q(x) is the heat source or sink term as a function of position x (in watts per meter, W/m).
- k is the thermal conductivity of the material (in watts per meter per degree Celsius, W/(m⋅°C)).
The code examples I provided earlier assumed steady-state conditions, which means ∂t∂T​=0, leading to a simplified equation:
0=α∂x2∂2T​+kq(x)​
This simplification is valid when the temperature distribution no longer changes with time, but the steady-state temperature profile is still influenced by the heat source and material properties.